Users Manual
Micrel KSZ8695 ARM9 SoC with ALTERA Cyclone IV FPGA
Brought to You By ORSoC

Legal Notices and Disclaimers
Copyright Notice
This ebook is Copyright © 2012 ORSoC
General Disclaimer
The Publisher has strived to be as accurate and complete as possible in the creation of this ebook, notwithstanding the fact that he does not warrant or represent at any time that the contents within are accurate due to the rapidly changing nature of information.
The Publisher will not be responsible for any losses or damages of any kind incurred by the reader whether directly or indirectly arising from the use of the information found in this ebook.
This ebook is not intended for use as a source of legal, business, accounting, financial, or medical advice. All readers are advised to seek services of competent professionals in the legal, business, accounting, finance, and medical fields.
No guarantees of any kind are made. Reader assumes responsibility for use of the information contained herein. The Publisher reserves the right to make changes without notice. The Publisher assumes no responsibility or liability whatsoever on the behalf of the reader of this report.

# Overview
Formfactor: SO-DIMM 200
Possible mating connector:
Manufacturer TE connectivity , part number 1565917-4
Available from DigiKey and Farnell/Newark:
http://www.digikey.se/product-detail/en/1565917-4/A97498TR-ND/1619799
http://se.farnell.com/te-connectivity-amp/1565917-4/memory-socket-so-dimm-200pos/dp/1677306?Ntt=1565917-4
The board will have the following key components:
1. Micrel KSZ8695P ARM9 SoC with builtin 4+1 Ethernet manageable switch
2. NEC uPD72010 USB 5 x USB 2.0 host ports
3. ALTERA Cyclone IV FPGA
4. SDRAM and NOR FLASH
5. Supply circuit

KSZ8695P
CycloneIV
UPD72010
NOR
FLASH
POL
POL
LDO
LDO
LDO
67.6mm

4+1 ETH

5xUSB

IO/LPC

Memory bus

Supply circuit support single cell Li+ battery. Board can be supplied from
1. AC connected power source
2. USB
3. Battery

# SO-DIMM pinout
## Supply
Pin #	Signal	Comment
1,2,3,4	BAT	For battery operation connect to single cell Li+ battery. For no battery operation connect to BAT_SENSE and leave floating. Voltage 2.7-5.5V
5	BAT_SENSE	Battery voltage sense
6	TS	Battery temperature sense
7,8,9, 10	AC	Connect to AC connected power source, 4.3-5.8V
11,12, 13,14	USB	VBUS USB power source, 4.3-5.8V. / If unused connect to GND
15	SDA	I2C manage bus
16	IRQ	Power circuit IRQ
17	SCL	I2C manage bus
18	RESETN	Board reset, active low
19	PB_IN	Push button to cycle power.
20	GND
21	WLEDSRC1	White LED source 1
22	WLEDSINK1	White LED sink 1
23	WLEDSRC2	White LED source 2
24	WLEDSINK2	White LED sink 2
25,26, 27,28	1.8V	1.8V supply from on board source
29,30, 31,32	3.3V	3.3V supply from on board source
33	1.8VA	1.8V from on board LDO
34	3.3VA	3.3V from on board LDO
35	LDO3/SW1	Connected to on board LDO/power switch
36	LDO4/SW2	Connected to on board LDO/power switch
38,40	GND
63,65	VCCIOB1	VCC IO bank1, FPGAIO[0:21]
64,66	GND
92,94	GND
115,116,117,118	GND
139,140	GND
148,156,162, 164,170,172, 178,180,198, 200	GND

## FPGA IO
### Clock sources
Pin #	Signal	Comment
37	CLK0/CLK0P	External clock source
39	CLK1/CLK0M	External clock source

### Bank 1
Pin #	Signal	Comment
41	FPGAIO0
43	FPGAIO1
45	FPGAIO2
47	FPGAIO3
49	FPGAIO4
51	FPGAIO5
53	FPGAIO6
55	FPGAIO7
57	FPGAIO8
59	FPGAIO9
61	FPGAIO10
42	FPGAIO11
44	FPGAIO12
46	FPGAIO13
48	FPGAIO14
50	FPGAIO15
52	FPGAIO16
54	FPGAIO17
56	FPGAIO18
58	FPGAIO19
60	FPGAIO20
62	FPGAIO21

### Bank 2

Pin #	Signal	Comment
67	GXB_TX3P / FPGAIO22	Reserved for high speed signals
69	GXB_TX3N / FPGAIO23	Reserved for high speed signals
71	GXB_RX3P / FPGAIO24	Reserved for high speed signals
73	GXB_RX3N / FPGAIO25	Reserved for high speed signals
75	GXB_TX2P / FPGAIO26	Reserved for high speed signals
77	GXB_TX2N / FPGAIO27	Reserved for high speed signals
79	GXB_RX2P / FPGAIO28	Reserved for high speed signals
81	GXB_RX2N / FPGAIO29	Reserved for high speed signals
83	GXB_TX1P / FPGAIO30	Reserved for high speed signals
85	GXB_TX1N / FPGAIO31	Reserved for high speed signals
87	GXB_RX1P / FPGAIO32	Reserved for high speed signals
89	GXB_RX1N / FPGAIO33	Reserved for high speed signals
91	GXB_TX0P / FPGAIO34	Reserved for high speed signals
93	GXB_TX0N / FPGAIO35	Reserved for high speed signals
95	GXB_RX0P / FPGAIO36	Reserved for high speed signals
97	GXB_RX0N / FPGAIO37	Reserved for high speed signals
99	FPGAIO38
101	FPGAIO39
103	FPGAIO40
105	FPGAIO41
68	FPGAIO45
70	FPGAIO46
72	FPGAIO47
74	FPGAIO48
76	FPGAIO49
78	FPGAIO50
80	FPGAIO51
82	FPGAIO52
84	FPGAIO53
86	FPGAIO54
88	FPGAIO55
90	FPGAIO56
96	FPGAIO57
98	FPGAIO58
100	FPGAIO59
102	FPGAIO60
104	FPGAIO61
106	FPGAIO62

### Low Pin Count, LPC

Pin #	Signal	Comment
107	FPGAIO42/ LAD[3]
108	FPGAIO63/ LAD[2]
109	FPGAIO43/ LAD[1]
110	FPGAIO64/ LAD[0]
111	FPGAIO44/ LFRAME
112	FPGAIO65/ SER_IRQ
113	PCLKOUT	PCI Clock source
114	PRSTN	PCI reset, active low

## USB
Pin #	Signal	Comment
119,123,127, 131,135	DP[1:5]	D+ USB host [1:5]
121,125,129, 133,137	DM[1:5]	D- USB host [1:5]
120,124,128, 132,136	OC[1:5]	USB over current [1:5], input
122,126,130, 134,138	PP[1:5]	USB port power [1:5], output

## Ethernet
Pin #	Signal	Comment
141	WANRXP	WAN port RX+
143	WANRXM	WAN port RX-
145	WANTXP	WAN port TX+
147	WANTXM	WAN port TX-
142,144	WLED[0:1]	WAN LED indicators
146	WANFXSD	WAN FX signal detect
149,157, 165,173	LANRXP[1:4]	LAN port [1:4] RX+
151,159, 167,175	LANRXM[1:4]	LAN port [1:4] RX-
153,161, 169,177	LANTXP[1:4]	LAN port [1:4] TX+
155,163, 171,179	LANTXM[1:4]	LAN port [1:4] TX-
154	LANFXSD1	LAN port 1 FX signal detect
150,152	L1LED[0:1]	LAN port 1 LED indicators
158,160	L2LED[0:1]	LAN port 2 LED indicators
166,168	L3LED[0:1]	LAN port 3 LED indicators
174,176	L4LED[0:1]	LAN port 4 LED indicators

## CPU
Pin #	Signal	Comment
181	GPIO0	GPIO0/EINT0
182	GPIO1	GPIO1/EINT1
183	GPIO2	GPIO2/EINT2
184	GPIO3	GPIO3/EINT3
185	GPIO4	GPIO4/TOUT0
186	GPIO5	GPIO5/TOUT1
187	GPIO6
188	GPIO7
189	GPIO8
190	GPIO9
191	GPIO10
192	GPIO11
193	GPIO12
194	GPIO13
195	GPIO14
196	GPIO15

## Config/Debug
Pin #	Signal	Comment
197	USBDBGDP	USB D+
199	USBDBGDM	USB D-

# Recommended Resources
ORSoC – http://www.orsoc.se
ORSoC is a fabless ASIC design & manufacturing services company, providing RTL to ASIC design services and silicon fabrication service. ORSoC are specialists building complex system based on the OpenRISC processor platform.
Open Source IP – http://www.opencores.org
Your number one source for open source IP and other FPGA/ASIC related information.