SD/eMMC/MMC Card hardware testing unit

MMC Test Pack : synthesizable cores Technical Reference Manual

Written by:

John Clayton
Klugwhallah FPGA design team

March 17, 2017

# List of Acronymns
DDR	Double Data Rate
FPGA	Field Programmable Gate Array
JTAG	Joint Test Access Group
MMC	Multi-Media Card
SD	Secure Digital
USART	Universal Synchronous/Asynchronous Receiver/Transmitter
VHDL	VHSIC Hardware Description Language
VHSIC	Very High Speed Integrated Circuit

# Introduction
This document provides a description of the interface signals, internal structure and registers present in the synthesizable cores within the VHDL package file named “mmc_test_pack.vhd” Some of the cores may be intended for use at lower levels of a design, in hierarchical fashion. All cores in the VHDL package are synthesizable and have been tested via simulation and in hardware using a Xilinx “ARTY” Artix 7 FPGA development board.
# Description of Cores
## Background
The “mmc_test_pack.vhd” VHDL package consists of two VHDL entities which combine with other cores from “sd_card_pack.vhd,” “sd_host_pack.vhd” and nine other VHDL packages, to realize a core that facilitates simulation, hardware testing and data logging of traffic on a Multi-Media Card (MMC) or Secure Digital (SD) card bus. The main specification document used during development was the JEDEC document JESD84-A44 titled “Embedded MultiMediaCard(e•MMC)” (MMCA, 4.4) version.
## Summary of Cores In Package
The cores present in the package file “mmc_test_pack.vhd” are shown in table Table 1. The last core in the table was written specifically for the task at hand, namely to provide an FPGA based data logger and test platform for working with SD/MMC hosts and cards. The functional capability of the mmc_tester core is such that it can be used in several different ways.

Name	Description
mmc_test_cmd_rx	Card command receiver core, testing version
mmc_tester	Card and host testing, card datalogging core

Table 1: MMC Test Pack Cores

## mmc_test_cmd_rx
The first core is one of the most elementary and basic, a special testing version of a SD/MMC command receiver. Its internal structure is shown in this block diagram:

47 bit shift register
Start bit detector (countdown load)
6 bit down counter

SD/MMC Command Signal and clock input
CRC-7 checker

Output Latch

cmd_raw_o
stop_err_o
crc_err_o
stop bit check

cmd_done_o

The mmc_test_cmd_rx captures all traffic going across the bus in either direction, both commands and responses, and it attempts to correctly capture the first 48 bits of the communication. This was done as a trade off, so that all traffic could be captured in 48 bit segments, and longer 136 bit messages are simply truncated in the interest of simplicity. Just to reiterate, the mmc_test_cmd_rx captures traffic from both directions, and has logic to correctly ignore the “tail end” of longer messages, and in these ways it differs from the “regular” sd_card_cmd_rx receiver in sd_card_pack.vhd.

This module is meant to be part of a system that tests, or snoops on an SD/MMC card.

This module clocks incoming serial bits from the cmd signal into a 48 bit shift register. It starts when a '0' (start) bit is found, and then shifts in 47 additional bits. The expected format of the command is:

0 d [index] [arg] [crc] 1

Where:
   d	= direction bit. '1'=host to card, '0'=reply from card.
   index	= 6 bits
   arg	= 32 bits
   crc	= 7 bits

The test command receiver checks that the last bit is a '1' (stop) bit, in the expected position (bit 47; start bit is bit 0). The seven bits immediately prior to the stop bit are checked using a CRC-7 code.
If any of the checks do not pass, the associated error bits are set. Regardless of errors, however, the received data bits are presented at the cmd_raw_o output. The cmd_rx_done_o output is pulsed high for one clock cycle to notify the downstream entities that newly received data is available.

In the interest of simplicity and in an effort to remain practical, only 48 bit responses are captured correctly by this unit. For R2 responses, which are 136 bits long, only the first 48 bits are presented.
Because the R2 type responses are 136 bits long, specific logic is included to try and detect them, and prevent errors from being flagged by their occurrence. The first eight bits of an R2 response are "00111111". Unfortunately, the first eight bits of a 48 bit R3 response are also "00111111". Fortunately, the CRC field of an R3 response is always set to "1111111". So, the logic checks for these conditions and behaves accordingly. In the case of an R2 response, that includes ignoring further activity on the command line for another 88 clocks after the initial 48 bits are received.

Note that this receiver runs entirely within the sd_clk_i clock domain. Therefore, care must be taken when using the outputs. A FIFO can form a natural "clock domain boundary crossing" or the user may need to implement other special handshaking to safely transfer signals into a different clock domain.
## mmc_tester
Now, we get into the real “meat” of this VHDL package.
This core, mmc_tester, is a synthesizable top level unit which brings together many useful pieces in order to allow testing of devices which share an MMC cardbus. It also allows snooping of the traffic over that bus, providing a means for sending out the resulting timestamped “telemetry” for archiving. To approach the structure of this core in an analytical way, it will help to state, at the outset, that the lower level units which compose the mmc_tester comprise five main functions:
1. An sd_controller_8bit_bram core as an MMC host, with some BRAM connected to give the host some storage area, plus some registers to allow working with the host.
2. An mmc_data_pipe core, which includes an sd_card_emulator, plus some BRAM and FIFOs for use as an emulated MMC device.
3. A main system parellel bus, with automatic baud rate enabled async_syscon system controller, which communicates with registers and BRAM and/or FIFOs in both the host and the data pipe cores. The system controller is a “hardware debugger” unit, which implements a minimal command set via an asynchronous serial communications terminal.
4. An mmc_test_cmd_rx, which can “snoop” on the MMC command bus. The timestamped output of the MMC command snooper is buffered in a small FIFO, and then periodically sent out for archiving elsewhere by means of an asynchronous serial transmitter connected to a separate serial port (This is essentially the transmit half of a UART.) Statistics counters are also provided tracking the number of good messages, the number with CRC errors, and the number with stop bit errors.
5. A set of I/O muxes, which can be controlled via registers accessible over the main bus, or by physical switches on the FPGA board, allowing “crossbar steering” of the MMC bus. By means of these muxes, the internal MMC host can be used with an external MMC card, or the external MMC bus can be used with the internal mmc_data_pipe core, or the internal MMC host and the internal MMC data pipe core can be used with each other.
The sheer scope of this mmc_tester core makes it difficult to explain fully, but with careful understanding of its components, the purpose and usefulness of the different settings and facilities it provides should become clear. It also aids understanding to study the memory map of the items connected to the system bus which is controlled by the hardware debugger.
The block diagram of this core is:

Crossbar Mux
Logic
MMC bus
SD/MMC
host
core

MMC data pipe core
(slave)

snooped cmd FIFO buffer
MMC test cmd receiver

telemetry encoder
SD/MMC host BRAM

serial com
(bi-directional)

asynchronous telemetry sender
snooped telemetry
cmd/data message statistics counters

t-stamp capture

tester registers

        Main System Bus

async_syscon serial connected system controller

Auto-baud generator

For simplicity, the register connections, and the “flancters” used for safe clock domain crossing are not shown in this block diagram. There are two main clock domains in this core, the first being the SD/MMC cardbus clock domain, which is used by substantial parts of the MMC host and MMC slave cores, and the second being the FPGA system clock, which is used by the rest of the system, including the async_syscon system controller, the telemetry sender, and all the registers.

A compact summary of the mmc_tester memory map is given here:
Address	Length	Function
0x03000000	0x10	SD/MMC host core registers
0x03000010	0x10	SD/MMC slave core registers
0x03000020	0x10	mmc_tester core registers
0x04000000	0x4000*	16k byte SD/MMC host BRAM (*Can be set by generics)
0x05000000	0x4000*	16k byte SD/MMC slave BRAM (*Can be set by generics)

Table 2: mmc_tester memory map “30,000ft overview”

The summary of the mmc_tester memory map is a good introduction to the way the components are mapped on the main system bus, but to be more helpful, the expanded memory map is given here. Note that further details on the different fields contained in SD/MMC host and slave registers are given in the sd_card_pack and sd_host_pack documents. The mmc_tester core registers are further explained using diagrams inside this document.

Address	Location	Function
0x03000000	SD/MMC host	SD/MMC transfer data block size
0x03000001	SD/MMC host	SD/MMC transfer data block count
0x03000002	SD/MMC host	SD/MMC command index
0x03000003	SD/MMC host	SD/MMC command argument
0x03000004	SD/MMC host	Response register 0
0x03000005	SD/MMC host	Response register 1
0x03000006	SD/MMC host	Response register 2
0x03000007	SD/MMC host	Response register 3
0x03000008	SD/MMC host	SD/MMC bus size, reset, bustest and timeout settings
0x03000009	SD/MMC host	SD/MMC bus operating frequency
0x0300000A	SD/MMC host	SD/MMC command interrupt status register
0x0300000B	SD/MMC host	SD/MMC command interrupt enable register
0x0300000C	SD/MMC host	SD/MMC data interrupt status register
0x0300000D	SD/MMC host	SD/MMC data interrupt enable register
0x0300000E	SD/MMC host	DMA address register
0x0300000F	SD/MMC host	(Reserved)
0x03000010	SD/MMC slave	Card reported status
0x03000011	SD/MMC slave	Card RCA and DSR registers
0x03000012	SD/MMC slave	Card EXT_CSD address
0x03000013	SD/MMC slave	Card EXT_CSD data
0x03000014	SD/MMC slave	Card CSD(31:0)
0x03000015	SD/MMC slave	Card CSD(63:32)
0x03000016	SD/MMC slave	Card CSD(95:64)
0x03000017	SD/MMC slave	Card CSD(127:96)
0x03000018	SD/MMC slave	(Reserved)
0x03000019	SD/MMC slave	(Reserved)
0x0300001A	SD/MMC slave	(Reserved)
0x0300001B	SD/MMC slave	(Reserved)
0x0300001C	SD/MMC slave	(Reserved)
0x0300001D	SD/MMC slave	(Reserved)
0x0300001E	SD/MMC slave	(Reserved)
0x0300001F	SD/MMC slave	(Reserved)
0x03000020	mmc_tester	LED register
0x03000021	mmc_tester	switch input register (read only)
0x03000022	mmc_tester	Host/slave enables, telemetry FIFO register access enable
0x03000023	mmc_tester	mmc_test_cmd_receiver command filter setting
0x03000024	mmc_tester	received command good count
0x03000025	mmc_tester	received command CRC bad count
0x03000026	mmc_tester	received command stop error bad count
0x03000027	mmc_tester	data block transfer count
0x03000028	mmc_tester	MMC data bus size setting (write to reset)
0x03000029	mmc_tester	telemetry FIFO fill level (write to clear FIFO contents)
0x0300002A	mmc_tester	telemetry FIFO data read port (byte-wise shift register)
0x0300002B	mmc_tester	(RESERVED)
0x0300002C	mmc_tester	(RESERVED)
0x0300002D	mmc_tester	(RESERVED)
0x0300002E	mmc_tester	SD/MMC data pipe (internal slave) FIFO clear bits
0x0300002F	mmc_tester	SD/MMC data pipe (internal slave) FIFO read/write port

Table 3: mmc_tester memory map full register list
For each of the registers implemented within the mmc_tester, further explanation and a register diagram are given. Note that in this core, the parallel system bus is a 32-bit data and 32-bit address bus, with each function being allocated a block of 16 register addresses. Addresses in the system are 32-bit “double word” addresses, meaning that each address selects a specific 32-bit data word location, and there are no byte-enables or other byte addressing constructs. the address given for each register is the relative offset from the base address used to generate the 16-register block select signal:
### Register 0x0 : LED Register

Address 0x0300_0020 is R0, the LED outputs register (READ/WRITE). This register contains a number of bits meant for controlling LEDs on the test board, just for fun. The sixteen bits in this register are connected to the LEDs on the ARTY board. The four least significant bits are connected to the green LEDs, and the twelve most significant bits are connected to the RGB LEDs, as shown in Table 4. Note that the LEDs are in reality driven by a data selector which can select either the LED outputs register or the upper 32-bits of a 40-bit counter which runs at the ARTY system clock rate of 100 MHz. The selector is controlled by switch SW3, such that if SW3 is on the “OFF” position (slider handle positioned near the edge of the ARTY board) then the LEDs are all driven by the LED outputs register. On the other hand, if SW3 is “ON” then the LEDs are driven by the counter, which makes for a nice visual display and a direct confirmation that the ARTY board is running the target design.
An observer with delicate sensibilities might pose the question: Why are Xilinx ARTY specific LEDs connected to a register in this mmc_tester core, which is meant to be independent of any particular FPGA development board? The answer is that most FPGA development boards have some set of LEDs available for display purposes, and so the number of bits contained within this register is parameterized so that the user can easily connect it to any given FPGA development board, and drive up to 32 LEDs with it.

Bit	Connection
0	LD4 anode, green
1	LD5 anode, green
2	LD6 anode, green
3	LD7 anode, green
4	LD3, red
5	LD3, green
6	LD3, blue
7	LD2, red
8	LD2, green
9	LD2, blue
10	LD1, red
11	LD1, green
12	LD1, blue
13	LD0, red
14	LD0, green
15	LD0, blue

Table 4: ARTY LED connections

### Register 0x1 : Switch State

Address 0x0300_0021 is R1, the Switch State register. The Switch State register is read only, and its contents reflect the status of the ARTY switch inputs, in real time. There is no debouncing or filtering applied to these values. The switches are mapped to bits within the register as shown in Table 5.

Bit	Connection
0	SW0
1	SW1
2	SW2
3	SW3
4	BTN0
5	BTN1
6	BTN2
7	BTN3

Table 5: ARTY switch connections

An observer with an easily offended sense of design partition might pose the question: Why are Xilinx ARTY specific switches connected to a register in this mmc_tester core, which is meant to be independent of any particular FPGA development board? The answer is that many FPGA development boards have some set of switches available as inputs to the FPGA, and so the number of bits contained within this register is parameterized so that the user can easily connect it to any given FPGA development board, and receive up to 32 switch states with it.
Note that some of the switches are dedicated to special functions within the mmc_tester design. The special functions are summarized in Table 6.
Switch	Dedicated Function
SW1	MMC host core enable
SW2	MMC slave core (data pipe) enable
SW3	Drive the LEDs from counter. Also, send any traffic log data as asynchronous bytes.

Table 6: ARTY dedicated switch functions
The functions of SW1 and SW2 are also available via register bits in register 0x2.
### Register 0x2 : Function Enables
Address 0x0300_0022 is R2, the Function Enables register. Certain functions of the mmc_tester core can be enabled or disabled via setting or clearing bits in the Function Enables register.

Bit [0] = Slave Enable Reg. Setting this bit causes the internal MMC_data_pipe slave to be active on the SD/MMC bus.
Bit [1] = Host Enable Reg. Setting this bit causes the internal sd_controller_8bit_bram unit to be active on the SD/MMC bus.
Bits [3..2] = "00" (Reserved)
Bit [4] = Slave Enabled (READ ONLY). This bit is the logical OR of bit[0] and the slave_en_i input, which is connected to ARTY switch SW2. Thus we see that the MMC_data_pipe slave can be made active by the switch, or the register bit.
Bit [5] = Host Enabled (READ ONLY). This bit is the logical OR of bit[1] and the host_en_i input, which is connected to ARTY switch SW1. Thus we see that the sd_controller_8bit_bram host unit can be made active by the switch, or the register bit.
Bits [7..6] = "00" (Reserved)
Bit [8] = Telemetry log register read access enable. When this bit is set, then telemetry log FIFO contents can be read out via register R10 (0xA), and the asynchronous serial transmitter is disabled. When clear, the asynchronous serial transmitter has access to the telemetry log FIFO instead of register R10.
For inquiring minds that want to know, a further explanation of the operation of the enable bits may be helpful:
Register 2, bit[0] : "slave_en_reg"
When high, this bit causes the MMC slave to receive commands, and respond to them. When this bit is enabled, the MMC slave will drive signals onto mmc_cmd_o and mmc_dat_o, including driving the mmc_cmd_oe_o and mmc_dat_oe_o lines when appropriate. When this bit is low, the MMC slave cmd input will be held high, and the MMC slave will not have anything to do.
Register 2, bit[1] : "host_en_reg"
When high, this bit causes the MMC host to send commands, and receive responses to them. When this bit is enabled, the MMC host can drive signals onto mmc_cmd_o and mmc_dat_o, including driving the mmc_cmd_oe_o and mmc_dat_oe_o lines when appropriate. When this bit is low, the MMC host cmd output will be cut off from affecting mmc_cmd_o, and the MMC host will not be able to influence the MMC bus signals.
If both of these bits are low, then the only function active in this core is to monitor the mmc commands which occur on the MMC bus due to the action of any outside MMC hosts, such as card readers, which may send commands to an MMC card on the bus.
With "host_enable" set, the mmc_tester can be used to communicate with a real external SD/MMC device, perhaps for the purpose of reading or writing some sectors, or reading the device registers including the CID, CSD and the 512 byte EXT_CSD.
With "slave_enable" set, on the other hand, an MMC slave can be used with an external SD/MMC card reader. The MMC slave includes a small amount of RAM, plus a pair of FIFO buffers. Writing data to the card at addresses below the upper boundary of the RAM, simply places the data into RAM. Beyond the RAM upper boundary, the data goes into the write FIFO. Reading is handled the same way.
An alternative to using the register bits to enable the slave and host, is to use the input signals "slave_en_i" and "host_en_i", which are connected to ARTY switches. These signals are simply logically ORed with the slave_en_reg and host_en_reg register bits, to produce the read only bits “slave_enable” and “host_enable.”
### Register 0x3 : Test Command Receiver Filter
Address 0x0300_0023 is R3, the Test Command Receiver Filter register. This register is a filter which can serve to pass a desired set of commands through to the command log, rejecting all the rest. It is useful for homing in on a particular command of interest.

Bits [7:0] determine what type of command creates a "command event" for capture in the log. Except for the value of 0x80, setting bit [7] means "capture and count everything," including all command indices, in both directions.
Example settings:
0x81..0xFF => Capture and count everything.
0x80 => Capture and count nothing. Nada. Zilch.
0x7F => Capture and count all host-to-card commands
0x3F => Capture and count all card-to-host responses
0x59 => Capture and count CMD25 from host-to-card only
0x28 => Capture and count CMD40 R5 responses only
0x27 => Capture and count CMD39 R4 responses only
0x19 => Capture and count CMD25 R1 responses only
0x00 => Capture and count CMD0 R1 responses only

To explain more clearly how these filter settings work, it is helpful to recall that the first eight bits of the command or response are:
[0][d][cccccc]
Where:
0 = start bit (always low)
d = direction bit (1 for host to card, 0 for card response)
cccccc = command index, ranging from 0 to 56.
A special setting of 63 for the cccccc field, selects long responses and/or 48-bit R3 OCR responses. Therefore, since 136 bit long responses are not differentiated from 48-bit R3 OCR responses, it becomes clear that the design of the filter is not perfect. For example, there is no way to act on only R3 responses. However, there is really no need for a perfect filter. This one is, well, you know, good enough.

### Registers 0x4 – 0x7 : Transfer statistics registers
These four registers contain counts of different categories of transfers detected on the SD/MMC bus.

Address 0x0300_0024 (R4) is the Error-free Command Events count.
Address 0x0300_0025 (R5) is the Command Events with CRC error count.
Address 0x0300_0026 (R6) is the Command Events with stop bit error count.
Address 0x0300_0027 (R7) is the Number of data transfers completed count.

No clear means are provided for the mmc_tester to determine what direction the data is flowing over the SD/MMC data lines. Therefore, the R7 register simply contains the total number of transfers started in either direction. Note that this 32-bit counter is distinct from the eight bit "tlm_d_count" data transfer counter in the telemetry, which is a relative count, cleared at every command transfer event.

### Register 0x8 : SD/MMC data bus size register
This register allows the user of the mmc_tester to read the current SD/MMC data bus size. This register setting can only be altered to larger bus sizes by the action of the SD/MMC host, sending a SWITCH command. However, through the system bus interface, it can be cleared back to its default setting of “00.”

Address 0x0300_0028 is R8, the reg_dbus_size register.
Bits [1:0] reflect the current SD/MMC data bus size setting, as follows:
0 => 1 bit data bus transfers
1 => 4 bit data bus transfers
2 => 8 bit data bus transfers
In order for the mmc_tester to determine when a data transfer is completed, so that it can count valid start bits, it is required to know the data bus size. Logic is present to decode when a host-to-card command of index 6 (CMD6), the SWITCH command, is seen with an argument 0x03B70s00, where s contains the new data bus size. This 2-bit setting is then stored in the reg_dbus_size register, and decoded to set the "dstart_wait" parameter used for ignoring data bus activity during an active data transfer. The reg_dbus_size starts out at "00b", and is expected to change to "01b" for 4-bit SD/MMC activity, and to "10b" for 8-bit MMC activity. SD cards are restricted to 4-bit data bus width maximum.

### Register 0x9 : Traffic log FIFO fill level

This register allows the user of the mmc_tester to read the number of entries currently present in the traffic log, or “telemetry stream” FIFO. The size of this FIFO is currently set by a constant within the mmc_tester core at 16384 bytes. The FIFO receives and stores time stamped entries, each entry representing a command or data transaction detected on the SD/MMC bus. The format of the entries is explained further in the description of register 0xA.

### Register 0xA : Traffic log FIFO data

Address 0x0300_002A is R10, the SD/MMC traffic log FIFO read port. Telemetry bytes can be read out of the traffic log FIFO whenever enabled in R2 bit 8. For convenience in reading the data, the bytes are packed into 32-bit words. If R2 bit 8 is clear, then reading this register returns 0x55555555.
Each traffic log (A.K.A. telemetry stream) entry is composed of 16 bytes, shown in Table 7.

Slice Bytes	Payload	Name	Contents
[0..3]	32 bits	Sync Pattern	0xFE6B2840
[4]	8 bits	tlm_fid	Frame ID, a number which increments with each frame.
[5..7]	24 bits	tlm_tstamp	Timestamp, in μsec. Has a 16.777216 s rollover period.
[8]	8 bits	tlm_d_count	Data transfer count, cleared at every host command.
[9]	8 bits	tlm_code_byte	255 for host-to-card commands, 0 for card-to-host.
[10..15]	48 bits	t_rx_cmd_raw	Raw contents of the detected command.

Table 7: mmc_tester traffic log record format

The captured traffic log can be output via an asynchronous transmitter. If the tlm_fifo_reg_access bit is clear in register 0x2, and ARTY SW3 is turned on, the regular asynchronous serial response stream is immediately preempted by a stream of telemetry data spewing forth for capture on a host computer system. The binary data bytes are sent out using the same Baud rate as the established hardware debugger serial session, and there is no flow control, so the receiving software must be ready to buffer and store the data immediately. An example of some SD/MMC bus traffic log data captured into a file, as displayed in a binary editor, is shown in Figure 1.

Figure 1: SD/MMC traffic log file example

### Register 0xD : mmc_data_pipe write FIFO fill level

Address 0x0300_002D is R13, the mmc_data_pipe write data FIFO fill level. Reading this register returns the number of bytes in the MMC slave write data FIFO. The FIFO holds data that are meant to flow from the MMC slave to the host. Writing to this register clears the MMC slave write data FIFO.

### Register 0xE : mmc_data_pipe read FIFO fill level

Address 0x0300_002E is R14, the mmc_data_pipe read data FIFO fill level. Reading this register returns the number of bytes in the MMC slave read data FIFO. The FIFO holds data that have been sent from the host to the MMC slave. Writing to this register clears the MMC slave read data FIFO.

### Register 0xF : mmc_data_pipe FIFO data

Address 0x0300_002F is R15, the MMC_data_pipe FIFO data port. Writing to this address loads another byte into the MMC slave write data FIFO, thereby enqueueing it to be read by the host from the MMC slave. However, if the write data FIFO is full, then nothing happens, and the data bits are thrown into the "bit bucket." Reading from this address reads a byte, removes it from the MMC slave read data FIFO, which data was previously delivered from the host to the MMC slave. However, if the read data FIFO is empty, then no valid data is actually delivered, as can well be understood.