Artec Group OÜ, Türi 10c Tallinn, / 11313 Estonia European Union Tel: (+372) 6718 550 / Fax: (+372) 6718 555 / www.artecgroup.com / info@artecgroup.com	Programmable LPC Dongle / DATA SHEET / FPGA based hardware debugger platform

# Dongle version 4 Features:
- Supports LPC memory read (can be disabled),LPC Firmware Hub memory read
  and IO write for POST Code capture (postcode only mode can be enabled)
- 4 segment LED display for debug purposes
- 10 bit GPIO header for debug purposes
- Selectable voltage source either USB or LPC bus
- 4 jumper selectable boot images for LPC
- Third party free USB drivers for
  - Windows (98,2000,ME,XP)
  - Linux 2.40 and greater
Included:
- LPC Dongle
- Python based software with source (Linux and Windows supported)
- USB cable
- LPC cable

# LPC dongle interfaces
## LPC
Drawing 1: Board top layout
LPC header provides 7 IO pins used for LPC signal (see Dongle schematic). By default 1MB on flash can be accessed over LPC bus (highest MB of 4 MB available in each mode configuration). This can be changed by IO command to full 4 MB.
LPC IO write to address 0x0088 data 0xF4	turn on 4MB addressing
LPC IO write to address 0x0088 data 0xF1	turn off 4MB addressing
LPC IO write to address 0x0080 will be displayed on Post code byte
## Mode Select
Mode select jumpers are intended for internal image selection from dongle flash divided into 4 separate 4 MB sections.
## GPIO header
On GPIO header pin pairs 1-2 and 5-6 are used as jumper pins as shown on Drawing 1. Jumper on GPIO header J1 pin pair 1-2 is “Enable LPC Memory read” this is legacy option to allow booting from devices that don't support LPC Firmware Hub read cycles although LPC Firmware read cycles are also responded in this configuration. If pins 1-2 are left open only LPC Firmware read cycles are responded.
GPIO pins are platform pins that are not used in the standard LPC version of the dongle but are target for tailored development for specific functions.
## VCC source select
Jumper is used to define VCC source. When USB cable is used at the same time with target board LPC connection, JMP4 should be off. If jumper is on pins 1,2 (marked with thick white line under the pins) the VCC3V is taken from target system, but USB cable must be disconnected.
When target board is used as voltage source the POR (power on reset) time along with the FPGA configuration time has to be taken into account when using the dongle as a boot device. It is recommended to use target board reset to initiate clean boot after power up.
## USB
USB interface is used to program dongle flash or read back flash content. This can be done by Artec USB Dongle programming utility.
Usage:
Write file	dongle.py [-vq] -c <name> <file> <offset>
Readback file	dongle.py [-vq] -c <name> [-vq] -r <offset> <length> <file>
Options:
 <file> <offset>	When file and offset are given file will be written to dongle
file:	File name to be written to dongle
offset:	Specifies data writing starting point in bytes to 4M window
For ThinCan boot code the offset = 4M - filesize. To write
256K file the offset must be 3840K
 -c <name>	Indicate port name where the USB Serial Device is
name:	COM port name in Windows or Linux Examples: COM3,/dev/ttyS3
See Device Manager in windows for USB Serial Port number
 -v	Enable verbose mode. Displays more progress information
 -q	Perform flash query to see if dongle flash is responding
 -r <offset> <length> <file> Readback data. Available window size is 4MB
offset:	Hexademical offset byte addres inside 4MB window
length:	Amount in bytes to read starting from offset. Example: 1M
use M for MegaBytes, K for KiloBytes, none for bytes
file:	Filename where data will be written
 -e	Erase device. Erases Full 4 MegaBytes
Board test options:
 -t	Marching one and zero test. Device must be empty
To test dongle erase the flash with command -e
Enables dongle memory tests to be executed by user
 -b	Leave flash blanc after test. Used with option -t
Examples:
dongle.py -c COM3 loader.bin 0
dongle.py -c /dev/ttyS3 boot.bin 3840K
dongle.py -c COM3 -r 0x3C0000 256K flashcontent.bin

USB programming utility can address all of the 4 MB available in any mode that is selected. It must be remembered that only 3072KB to 4096 KB in each mode configuration is directly accessible over LPC and is repeated in LPC memory address space (x86 legacy 1M window) without using the 0xF4 command first (see LPC paragraph).
## Dongle version
Dongle version number can be seen on the postcode byte if reset button is held down while USB cable is connected or dongle is connected to a host system by LPC bus. This document deals with dongle version 4.
Additions from version 3 are:
- LPC Firmware Hub read capability and disable jumper to disable the new mode.
- Postcode only mode where read requests are not responded to only postcode bytes are shown
## FAQ
Q: Why does the dongle give error code when opening serial port in Ubuntu Linux?
A: If you use Ubuntu, make sure to uninstall brltty (apt-get remove brltty --purge) before you hook up the dongle; otherwise it will hijack the dongle and you won't be able to talk to it. Brltty is a software braille terminal. (http://www.coreboot.org/Artecgroup_programmable_LPC_dongle)
## Source code
Source code is available at http://www.opencores.org/projects.cgi/web/usb_dongle_fpga/overview
Contains:

- Python USB application source code
- VHDL LPC slave (supporting IO write and Memory read)
- VHDL Flash Waveform generator
- VHDL FTDI parallel interface to on-board flash (supports block write)
- VHDL Scanning LED segment display coder
- UCF file with pin location constraints (for Xilinx WEB pack)