Addr.	Bits	Description
0x00	[7...0]	SW jumper enable bits (set high to enable this bit to control jumper settings / will be automatically disabled if the physical jumper value changes)
0x01	[7...0]	SW jumper bits (set according to needed settings)
0x02	[0]	Enable Debug LED's (set '1' to enable debug led instead of jumper states)
	[7...1]	Reserved
0x03	[7...0]	Debug LEDs (set high to turn led on)
0x04	[7...0]	SW settings register