Big Counter IP Core
Specification

#### Author: Andrew Mulcock
amulcock@opencores.org

Rev. 0.1
January 1, 2008
##### Revision History
Rev.	Date	Author	Description
0.1	31-Dec-07	Andrew Mulcock	First Draft

Contents

# 1
Introduction

The BigCounter core is just that, a big counter, made up of the shift registers. This works well in such devices as the Xilinx range that contain SRL's.

Features:

- Small and fast.
- Pure VHDL, no special librares needed
- Tested with Xilinx XST 9.2 sp4

# 2
IO ports

## 2.1 Signals

Port	Width	Direction	Description
clk	1	Input	Block’s clock input
en_in	1	Input	High to allow counter to count
rco	no_of_stages-1	Output	Ripple carry out fomr each stage

## 2.2 Generics

Name	Type	Type	Description
No_of_stages	Integer	1 to 2**32	Number of divide by 16's needed

# 3
Architecture

This all started a LONG time ago, in the mid 1970's.

With a 40 MHz clock, I needed to produce a one clock wide pulse, ever 24192000000000 clocks. That required a 48 bit counter, counting up to 1600A3910000 hex. And believe me working that out in the mid 70's required more paper than you want to know about.

Anyway, the basic answer was a string of 16 74S163 counters.

Now these beasts have two active high enables( ENT and ENP ) , and one active high output ( RCO ). Both ENT and ENP must be high for the counter to count. The interesting thing is RCO is high when the counter is at terminal count ( F hex) and ENT is high. See Figure 1: basic 163 type counter which shows the two enables and the ripple carry out, but ignores the clock input.

Figure 1: basic 163 type counter

ent
enp
rco

Internally, they 163 is wired something like shown in Figure 2: Internals of a 163 counter.
This shows the two enables, and how the RCO is high when the counter is at B”1111” and input ent is high.

At first this seems strange, why two enables, and only one goes to the ripple carry out ? Well the answer is in how you can wire up the counters to get a fast counter.

You see normally with counters there is a frequency of operation against depth trade off, the bigger the counter gets, the more terms are needed at each stage. For a N stage counter, stage N need N-1 terms in it's enable

Figure 2: Internals of a 163 counter

&

rco(n)
&

ent(n)
enp(n)
clk_en(n)
counter

Q0

Q1

Q2

Q3
&

At first this seems strange, why two enables, and only one goes to the ripple carry out ? Well the answer is in how you can wire up the counters to get a fast counter.

You see normally with counters there is a frequency against depth trade off, the bigger the counter gets, the more terms are needed at each stage. For a N stage counter, stage N need N-1 terms in it's enable. With the '163', this was not the case, the frequency of operation depended on 1/( Trco + Tenp). Where Trco is the time of clock to output RCO being stable and Tenp is the set up time before clock needed on the enp input.

And the trick was in how you wired up the enable inputs to the rco outputs. See Figure 3.

Figure 3: wiring of 163 counters for high speed counting

enp
ent
rco

en
High
To further stages

enp
ent
rco

enp
ent
rco

enp
ent
rco

So where does this leave us ? If you look back at Figure 2, and replace the counter with a shift register, and initalise the shift register to all '0', one bit '1', then you have Figure 4.

Figure 4: shift register as a 163 counter
shift_srl(n)

Init x”0001”

&

rco(n)
&

ent(n)
enp(n)
clk_en(n)

Instead of the counter, we use a shift register, shift_srl. The enp and ent are still present, and anded together to form the single enable as before. The top bit of the shift register is feed around back to the beginning, and the top bit of the shift register anded together with the ent input, form the rco.

Now this fits rather well into Xilinx SRL's making very big counters very efficiently.

This is what the first half of the BigCounter performs, a cascade of divide by 16's formed out of shift registers.

## 3.1 Initialization

No reset is required, the core initializes in the FPGA to the correct levels This has been shown to work in Xilinx software, using the SRLs in Virtex devices.