SoC Debug Interface

Author: Igor Mohor

IgorM@opencores.org

Rev. 2.0

February 1, 2004

Copyright (C) 2001 - 2004 OPENCORES.ORG and Authors.

This document is free; you can redistribute it and/or modify it under the terms of the GNU General Public License as published by the Free Software Foundation; either version 2 of the License, or (at your option) any later version.

This document is distributed in the hope that it will be useful, but WITHOUT ANY WARRANTY; without even the implied warranty of MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the GNU General Public License for more details.

Revision History

| Rev. | Date | Author | Description |
| --- | --- | --- | --- |
| 0.1 | 02/02/01 | Igor Mohor | First Draft |
| 0.2 | 05/04/01 | IM | Trace port added |
| 0.3 | 16/04/01 | IM | WP and BP number changed, trace modified |
| 0.4 | 01/05/01 | IM | Title changed, DEBUG instruction added, scan chains changed, IO ports changed |
| 0.5 | 05/05/01 | IM | TSEL and QSEL register changed |
| 0.6 | 06/05/01 | IM | Ports connected to the OpenRISC changed |
| 0.7 | 14/05/01 | IM | MODER register changed, trace scan chain changed; SSEL register added |
| 0.8 | 18/05/01 | IM | RESET bit and signal added; STALLR changed to RISCOP |
| 0.9 | 23/05/01 | IM | RISC changed to OpenRISC; WISHBONE interface added, SPR and memory access added |
| 0.10 | 01/06/01 | IM | Meaning of Instruction status and Load/store status changed in all registers; more details added to Appendix A |
| 0.11 | 10/09/01 | IM | Register and OpenRISC scan chain operation changed |
| 1.0 | 19/09/01 | IM | Some registers deleted |
| 1.1 | 15/10/01 | IM | WISHBONE interface added; RISC Stall signal is set by breakpoint and reset by writing 0 to RISCOP register |
| 1.2 | 03/12/01 | IM | Chain length changed so additional CRC checking can be performed |
| 1.3 | 21/01/02 | Jeanne Wiegelmann | Document revised. |
| 1.4 | 07/05/02 | IM | Register MONCNTL added. |
| 1.5 | 10/10/02 | IM | WISHBONE Scan Chain changed to show state of the access. |
| 1.6 | 06/11/02 | IM | TRST_PAD_I changed from active low signal to active low signal. |
| 1.7 | 23/09/03 | Simon Srot | Mutliple CPU support added, WB 16-bit and 8-bit access possible through WBCNTL register use. |
| 2.0 | 01/02/04 | IM | New version of debug interface. Document name changed, Document split into two documents, one for TAP and one for debug. |

Contents

1	7

Introduction	7

2	8

IO Ports	8

2.1 TAP Ports	8

2.2 CPU Ports	9

2.3 WISHBONE Ports	9

3	11

Registers	11

3.1 CPU Registers List	11

3.2 CPU Operation Register	12

3.3 CPU Select Register	12

4	14

Operation	14

4.1 Chain Selection	14

4.2 WISHBONE Sub-module	15

4.2.1 WISHBONE Read operation	16

4.2.2 WISHBONE Write operation	17

4.2.3 WISHBONE Status operation	19

4.2.4 Data and select signals	20

4.3 CPU Sub-module	2

4.3.1 CPU Read and CPU Register Read operation	3

4.3.2 CPU or CPU Register Write operation	4

4.3.3 Stalling CPU(s)	6

4.3.4 Resetting CPUs	6

4.3.5 Selecting different CPUs	6

5	8

Architecture	8

5.1 Debug Interface	10

5.2 CRC sub-module	10

5.3 WISHBONE sub-module	10

Introduction

The Development Interface is used for debugging purposes and is as such an interface between the processor(s), peripheral cores, and any commercial debugger/emulator or BS testing device. The external debugger or BS tester connects to the core via a fully IEEE 1149.1 compatible JTAG TAP port that is not part of this core. TAP is available at the opencores, too.

IO Ports

## 2.1 TAP Ports

Debug interface connects to the TAP controller with the following signals:

| Port | Width | Direction | Description |
| --- | --- | --- | --- |
| tck_i | 1 | input | Test clock input |
| tdi_i | 1 | input | Test data input |
| tdo_o | 1 | output | Test data output |
| shift_dr_i | 1 | input | TAP controller state “Shift DR” |
| pause_dr_i | 1 | input | TAP controller state “Pause DR” |
| update_dr_i | 1 | input | TAP controller state “Update DR” |
| debug_select_i | 1 | input | Instruction DEBUG is activated |

Table 1: TAP Ports

## 2.2 CPU Ports

| Port | Width | Direction | Description |
| --- | --- | --- | --- |
| cpu_clk_i | 1 | input | CPU clock signal. |
| cpu_addr_o | 32 | output | CPU address |
| cpu_data_i | 32 | input | CPU data input (data from CPU) |
| cpu_data_o | 32 | output | CPU data output (data to CPU) |
| cpu_bp_i | 1 | input | CPU breakpoint |
| cpu_stall_o | 1 | output | CPU stall (selected CPU is stalled) |
| cpu_stall_all_o | 1 | output | CPU stall all (all unselected CPUs are stalled) |
| cpu_stb_o | 1 | output | CPU strobe |
| cpu_sel_o | 8 | output | CPU select signals (one hot), select the CPU |
| cpu_we_o | 1 | output | CPU write enable signal indicates a write cycle when asserted high (read cycle when low). |
| cpu_ack_i | 1 | input | CPU acknowledge (signals end of cycle) |
| cpu_rst_o | 1 | output | CPU reset output (resets CPU) |

Table 2: CPU Ports

## 2.3 WISHBONE Ports

| Port | Width | Direction | Description |
| --- | --- | --- | --- |
| wb_clk_i | 1 | input | WISHBONE clock |
| wb_rst_i | 1 | input | WISHBONE reset |
| wb_ack_i | 1 | input | WISHBONE acknowledge indicates a normal cycle termination |
| wb_adr_o | 32 | output | WISHBONE address output |
| wb_cyc_o | 1 | output | WISHBONE cycle encapsulates a valid transfer cycle. |
| wb_dat_i | 32 | input | WISHBONE data input (data from WISHBONE) |
| wb_dat_o | 32 | output | WISHBONE data output (data to WISHBONE) |
| wb_err_i | 1 | input | WISHBONE error acknowledge indicates an abnormal cycle termination |
| wb_sel_o | 4 | output | WISHBONE select indicates which bytes are valid on the data bus. |
| wb_stb_o | 1 | output | WISHBONE strobe indicates a valid transfer. |
| wb_we_o | 1 | output | WISHBONE write enable indicates a write cycle when asserted high (read cycle when low). |
| wb_cab_o | 1 | output | WISHBONE consecutive address burst indicates a burst cycle. |
| wb_cti_o | 3 | output | WISHBONE cycle type identifier indicates type of cycle (single, burst, end of burst) |
| wb_bte_o | 2 | output | WISHBONE burst type extension |

Table 3: WISHBONE Ports

Registers

This section specifies all registers in the Debug Interface. There are currently two sub-modules in the debug interface, WISHBONE and CPU.

WISHBONE sub-module doesn’t have internal registers.

CPU sub-module does have internal registers and they are described in the following section.

## 3.1 CPU Registers List

| Name | Address | Width | Access | Description |
| --- | --- | --- | --- | --- |
| CPU_OP | 0x0 | 8 | R/W | CPU Operation Register |
| CPU_SEL | 0x1 | 8 | R/W | CPU Select Register |

Table 4: CPU Register List

## 3.2 CPU Operation Register

| Bit # | Access | Description |
| --- | --- | --- |
| 7:3 |  | Reserved |
| 2 | R/W | CPUSTALLALL – Stall all unselected CPUs 0 = normal operation 1 = Stall all unselected CPUs |
| 1 | R/W | RESET – Reset CPU 0 = normal 1 = reset |
| 0 | R/W | CPUSTALL – CPU Stall 0 = normal operation 1 = Stall CPU. CPU can also set this bit by inserting the cpu_bp_i signal. |

Table 5: CPU_OP Register

Reset Value:

CPU_OP: 00h

## 3.3 CPU Select Register

| Bit # | Access | Description |
| --- | --- | --- |
| 7:0 | R/W | CPUSEL – Select one CPU 00000001b = Selects CPU 0 (cpu_sel_o [0] is active) 00000010b = Selects CPU 1 (cpu_sel_o [1] is active) 00000100b = Selects CPU 2 (cpu_sel_o [2] is active) 00001000b = Selects CPU 3 (cpu_sel_o [3] is active) 00010000b = Selects CPU 4 (cpu_sel_o [4] is active) 00100000b = Selects CPU 5 (cpu_sel_o [5] is active) 01000000b = Selects CPU 6 (cpu_sel_o [6] is active) 10000000b = Selects CPU 7 (cpu_sel_o [7] is active) 00000000b = NO CPU selected (cpu_sel_o [7:0] not active) |

Table 6: CPU_SEL Register

Reset Value:

CPU_SEL: 00h

Operation

This section describes the operation of the Debug Interface and its sub-modules.

## 4.1 Chain Selection

The debug interface is just an interface between the sub-module that is target specific and the TAP controller. Currently two sub-modules are connected to the debug interface, WISHBONE sub-module and CPU sub-module. Up to 8 sub-modules can be connected to the debug interface.

First thing to do is to select the sub-module. This is done with the chain select instruction. Following needs to be done prior to the chain select operation:

- instruction DEBUG needs to be activated in the TAP (refer to the IEEE 1149.1 Test Access Port documentation for more information)

Then the “chain select” instruction needs to be shifted-in through the TAP data chain:

- 1-bit with value 1

- 3-bit chain ID

- 32-bit CRC

After this the following is shifted out:

- 4-bit status

  - 1 if incoming CRC is OK, else 0

  - 1 if command was “chain select”, else 0

  - 1 if non-existing chain was selected, else 0

  - always 1

- 32-bit CRC that is related with the outgoing data

Data that is shifted out before the status is not important (all zeros).

All the data is shifted in/out with the MSB bit shifted first.

See sections 5.1 Debug Interface on page 10 and 5.2 CRC sub-module on page 10 for more details about the CRC.

## 4.2 WISHBONE Sub-module

There are three types of instruction in the WISHBONE sub-module:

- “Set address/length/type” instruction

- “Go” instruction

- “Read status” instruction

Before some data can be read from or write to the WISHBONE, the following needs to be done:

- instruction DEBUG needs to be activated in the TAP (refer to the IEEE 1149.1 Test Access Port documentation for more information)

- WISHBONE sub-module needs to be selected (refer to section 4.1 Chain Selection on page 14 for more details)

All WISHBONE operations (except status read) consist of two consequent instructions. First instruction sets the address, type of instruction and length of data that is read or written. Second instruction is a “GO” instruction that actually does what the first instruction requests. Following section describes how read, write or status operations are performed.

### 4.2.1 WISHBONE Read operation

After the debug is enabled and WISHBONE selected (see description on page 15), two instructions need to be executed.

First instruction that sets the address, type of operation and length is performed by shifting the following data through the data scan chain:

- 1-bit with value 0

- 3-bit instruction (READ8, READ16, READ32, depending on the cycle type (32-bit, 16-bit or 8-bit))

- 32-bit address

- 16-bit length (describes data length in bytes)

- 32-bit CRC

After this the following is shifted out:

- 4-bit status

  - 1 if incoming CRC is OK, else 0

  - 3 bit-s of 0

- 32-bit CRC that is related with the outgoing data

Data that is shifted out before the status is not important (all zeros).

All the data is shifted in/out with the MSB bit shifted first.

Second instruction is a “GO” instruction and performs the read operation on the WISHBONE bus. Address, cycle type and data length are specified with the first instruction. Data is latched to the internal buffer. The “GO” instruction would look like this:

- 1-bit with value 0

- 3-bit instruction GO

- 32-bit CRC

After this the following is shifted out:

- data length x 8 bits of data

- 4-bit status

  - 1 if incoming CRC is OK, else 0

  - 1 if WISHBONE cycle didn’t finish (still in progress), else 0. This is important only for the first data byte

  - 1 if under run occurred (data couldn’t be read fast enough), else 0

  - 1 if WISHBONE error occurred

- 32-bit CRC that is related with the outgoing data

Data that is shifted out before the status is not important (all zeros).

All the data is shifted in/out with the MSB bit shifted first.

See sections 5.1 Debug Interface on page 10 and 5.2 CRC sub-module on page 10 for more details about the CRC.

### 4.2.2 WISHBONE Write operation

After the debug is enabled and WISHBONE selected (see description on page 15), two instructions need to be executed.

First instruction that sets the address, type of operation and length is performed by shifting the following data through the data scan chain:

- 1-bit with value 0

- 3-bit instruction (WRITE8, WRITE16, WRITE32, depending on the cycle type (32-bit, 16-bit or 8-bit))

- 32-bit address

- 16-bit length (describes data length in bytes)

- 32-bit CRC

After this the following is shifted out:

- 4-bit status

  - 1 if incoming CRC is OK, else 0

  - 3 bit-s of 0

- 32-bit CRC that is related with the outgoing data

Data that is shifted out before the status is not important (all zeros).

All the data is shifted in/out with the MSB bit shifted first.

Second instruction is a “GO” instruction and performs the write operation on the WISHBONE bus. Address, cycle type and data length are specified with the first instruction. Data that needs to be written to the WISHBONE bus is shifted in with the “GO” instruction. In this case the “GO” instruction looks like this:

- 1-bit with value 0

- 3-bit instruction GO

- data length x 8 bits of data

- 32-bit CRC

After this the following is shifted out:

- 4-bit status

  - 1 if incoming CRC is OK, else 0

  - 1 if WISHBONE cycle didn’t finish (still in progress), else 0. This is important only for the first data byte

  - 1 if over run occurred (data couldn’t be write fast enough), else 0

  - 1 if WISHBONE error occurred

- 32-bit CRC that is related with the outgoing data

Data that is shifted out before the status is not important (all zeros).

All the data is shifted in/out with the MSB bit shifted first.

See sections 5.1 Debug Interface on page 10 and 5.2 CRC sub-module on page 10 for more details about the CRC.

### 4.2.3 WISHBONE Status operation

After the debug is enabled and WISHBONE selected (see description on page 15), two instructions need to be executed.

Status operation consists of only one instruction that looks like this::

- 1-bit with value 0

- 3-bit instruction STATUS

- 32-bit CRC

After this the following is shifted out:

- 4-bit status

  - 1 if incoming CRC is OK, else 0

  - 1 if WISHBONE cycle didn’t finish (still in progress), else 0. This is important only for the first data byte

  - 1 if over run (under run) occurred (data couldn’t be write (read) fast enough), else 0

  - 1 if WISHBONE error occurred

- 32-bit CRC that is related with the outgoing data

Data that is shifted out before the status is not important (all zeros).

All the data is shifted in/out with the MSB bit shifted first.

Errors are always latched and hold until the status operation is performed (i.e. If WISHBONE error occurs, WISHBONE error bit remains set until the status operation is performed).  After the status operation, status bits are automatically cleared to zero.

See sections 5.1 Debug Interface on page 10 and 5.2 CRC sub-module on page 10 for more details about the CRC.

### 4.2.4 Data and select signals

Data in the WISHBONE sub-module is organized in the big endian byte ordering. Following section describes the data and select signals depending on the address and  type of operation (32-bit, 16-bit and 8-bit).

32-bit access (wb_adr_o[1:0] = 00b):

wb_sel_o[3:0] = 1111b

wb_dat _x[31:0] are used

16-bit access (wb_adr_o[1:0] = 00b):

wb_sel_o[3:0] = 1100b

wb_dat_x[31:16] are used

16-bit access (wb_adr_o[1:0] = 10b):

wb_sel_o[3:0] = 0011b

wb_dat_x[15:0] are used

8-bit access (wb_adr_o[1:0] = 00b):

wb_sel_o[3:0] = 1000b

wb_dat_x[31:24] are used

8-bit access (wb_adr_o[1:0] = 01b):

wb_sel_o[3:0] = 0100b

wb_dat_x[23:16] are used

8-bit access (wb_adr_o[1:0] = 10b):

wb_sel_o[3:0] = 0010b

wb_dat_x[15:8] are used

8-bit access (wb_adr_o[1:0] = 11b):

wb_sel_o[3:0] = 0001b

wb_dat_x[7:0] are used

## 4.3 CPU Sub-module

CPU sub-module consists of internal registers and the CPU interface.

It can make accesses to both internal CPU registers and the CPU interface.

Internal registers are used for:

- selecting one of the connected CPUs

- resetting the CPU(s)

- stalling the selecting CPU

- stalling all unselected CPUs

Before the CPU can be debugged, it must be selected. Selection is made through the write operation to the CPU register (See section 4.3.2 CPU or CPU Register Write operation on page 4 for more details).

CPU interface is an interface to the CPU debug facilities (that are part of the CPU).

Before some data can be read from or write to the CPU (registers or interface), the following needs to be done:

- instruction DEBUG needs to be activated in the TAP (refer to the IEEE 1149.1 Test Access Port documentation for more information)

- CPU sub-module needs to be selected (refer to section 4.1 Chain Selection on page 14 for more details)

There are two types of instruction in the CPU sub-module:

- “Set address/length/type” instruction

- “Go” instruction

CPU operation (read, write, register read or register write) consist of two consequent instructions. First instruction sets the address, type of instruction and length of data that is read or written. Second instruction is a “GO” instruction that actually does what the first instruction requests. Following section describes how read or write operations are performed.

### 4.3.1 CPU Read and CPU Register Read operation

After the debug is enabled and CPU sub-module selected (see description on page 15), two instructions need to be executed.

First instruction that sets the address and type of operation is performed by shifting the following data through the data scan chain:

- 1-bit with value 0

- 3-bit instruction (CPU_READ8, CPU_READ32 or CPU_READ_REG) depending on the cycle type (32-bit or 8-bit access to the CPU or 8-bit access to the CPU register))

- 32-bit address

- 32-bit CRC

After this the following is shifted out:

- 4-bit status

  - 1 if incoming CRC is OK, else 0

  - 3 bit-s 010b

- 32-bit CRC that is related with the outgoing data

Data that is shifted out before the status is not important (all zeros).

All the data is shifted in/out with the MSB bit shifted first.

Second instruction is a “GO” instruction and performs the read operation to the CPU interface or CPU registers. Address and cycle type are specified with the first instruction. Data is latched to the internal buffer. The “GO” instruction would look like this:

- 1-bit with value 0

- 3-bit instruction GO

- 32-bit CRC

After this the following is shifted out:

- 8 or 32 bits of data (CPU_READ32 returns 32-bits, CPU_READ8 and CPU_READ_REGreturn 8-bit data)

- 4-bit status

  - 1 if incoming CRC is OK, else 0

  - 3 bit-s 010b

- 32-bit CRC that is related with the outgoing data

Data that is shifted out before the status is not important (all zeros).

All the data is shifted in/out with the MSB bit shifted first.

See section 3.1 CPU Registers List on page 11 for description of the CPU registers.

See sections 5.1 Debug Interface on page 10 and 5.2 CRC sub-module on page 10 for more details about the CRC.

### 4.3.2 CPU or CPU Register Write operation

After the debug is enabled and CPU selected (see description on page 15), two instructions need to be executed.

First instruction that sets the address and the type of operation is performed by shifting the following data through the data scan chain:

- 1-bit with value 0

- 3-bit instruction (CPU_WRITE8, CPU_WRITE32 or CPU_WRITE_REG) depending on the cycle type (32-bit or 8-bit access to the CPU or 8-bit access to the CPU register))

- 32-bit address

- 32-bit CRC

After this the following is shifted out:

- 4-bit status

  - 1 if incoming CRC is OK, else 0

  - 3 bit-s of 010b

- 32-bit CRC that is related with the outgoing data

Data that is shifted out before the status is not important (all zeros).

All the data is shifted in/out with the MSB bit shifted first.

Second instruction is a “GO” instruction and performs the write operation to the CPU interface or CPU registers. Address and cycle type are specified with the first instruction. Data that needs to be written to the is shifted in with the “GO” instruction. In this case the “GO” instruction looks like this:

- 1-bit with value 0

- 3-bit instruction GO

- 8 or 32 bits of data

- 8 or 32 bits of data (CPU_WRITE32 needs 32-bits, CPU_WRITE8 and CPU_WRITE_REG need 8-bit data)

- 32-bit CRC

After this the following is shifted out:

- 4-bit status

  - 1 if incoming CRC is OK, else 0

  - 3 bit-s of 010b

- 32-bit CRC that is related with the outgoing data

Data that is shifted out before the status is not important (all zeros).

All the data is shifted in/out with the MSB bit shifted first.

See sections 5.1 Debug Interface on page 10 and 5.2 CRC sub-module on page 10 for more details about the CRC.

### 4.3.3 Stalling CPU(s)

The selected CPU can be stalled in two ways:

By deliberately setting bit CPUSTALL in the CPU_OP register to 1 (see section 3.2 CPU Operation Register on page 12 for more details). Clearing this bit again restarts the CPU.

An input breakpoint signal (cpu_bp_i) automatically stops the CPU and sets bit 0 of the CPU_OP register to 1. Clearing this bit again restarts the CPU.

When CPUSTALLALL bit is set in the CPU_OP register, all unselected CPUs are stalled.

For more information about the breakpoint generation refer to the CPU manual (i.e. OpenRISC 1000 System Architecture Manual).

### 4.3.4 Resetting CPUs

The Debug Interface puts the CPU to reset by setting the RESET bit in the CPU_OP register to 1. Clearing this bit to 0 deactivates the reset signal.

### 4.3.5 Selecting different CPUs

cpu_sel_o and cpu_stall_all_o signals have been added to the Debug Interface to support more than one CPU. It is meant, that this signals are used to enable muxing of all the signals going from/to CPU and Debug Interface (cpu_bp_i, cpu_data_i, cpu_data_o, cpu_addr_o, cpu_stall_o, cpu_ack_i). The muxing of signals is not part of the Debug Interface and is the responsibility of the system integrator.

cpu_sel_o signals are controlled from CPU_SEL register and cpu_stall_all_o signal is controlled from CPU_OP register.

Normally, if just one CPU is connected to the Debug Interface this signals are not necessary and can be ignored.

Architecture

The SoC Debug Interface architecture is based on IEEE Std. 1149.1 Standard Test Access Port and Boundary Scan Architecture. Other signals are added to provide additional flexibility.

The interface consists of several parts (blocks):

Logic that selects one of the connected scan chains (from sub-modules). Currently two sub-modules are available, CPU and WISHBONE.

CRC sub-module that checks incoming data.

CRC sub-module that calculates the CRC for the outgoing data.

WISHBONE sub-module

CPU sub-module

As seen on the following figure, debug interface is just one part of the complete debugging system. For more information about the TAP controller, go to the opencores web site. There is a complete IP core with test bench and documentation available.

If there are more than 1 CPU in the system, then additional external logic is needed (marked as MUX logic in the figure Figure 1: Complete system on page 9). The function of this logic is:

- Multiplexes data that comes from CPUs to data that goes to the debug interface.

- Defines stall signals that are connected to the CPUs from cpu_stall_o, cpu_stall_all_o and cpu_sel signals.

Figure 1: Complete system

## 5.1 Debug Interface

Debug Interface is an interface between the TAP controller and the sub-modules that are target specific (CPU, WISHBONE...). It receives data from the TAP whenever the DEBUG instruction is active (see IEEE 1149.1 Test Access Port documentation).

Data can hold two kinds of instructions:

- Chain select instruction

- Sub-module instruction

Chain select instruction is used for selecting/enabling the sub-module.

Sub-module instructions are sub-module specific. Each sub-module can use different instructions. Because of this, it is very easy to add additional sub-modules.

All the data (in both directions) is protected with the 32-bit CRC (see section 5.2 CRC sub-module on page 10 for more information). Both CRC engines (one for incoming data and one for outgoing data) are located in the debug interface. None of the sub-modules have its own CRC engine.

## 5.2 CRC sub-module

There are two CRC sub-modules in the debug interface. One is checking the incoming data, while the other is calculating the CRC from the outgoing data.

The following polynomial is used for 32-bit CRC calculation:

1 + x1 + x2 + x4 + x5 + x7 + x8 + x10 + x11 + x12 + x16 + x22 + x23 + x26 + x32

1-bit data input is used for CRC calculation. The MSB bit of data is shifted in/out first. The CRC is also received/send with MSB first.

There is more information about the CRC available in the 5.1 Debug Interface section on page 10).

## 5.3 WISHBONE sub-module

Is capable of doing the 8-bit, 16-bit and 32-bit WISHBONE accesses. All accesses are single accesses since the data flow through the TAP (JTAG) is slow and there is no need for bursts. Wishbone clock frequency must be higher than the TCK frequency. The length of the WISHBONE scan chain depends on the instruction (and their combination). See section 4.2 WISHBONE Sub-module on page 15 for more information about the chain length.

# Text boxes

Boundary Scan Chain

TRSTn

TMS

TCK

TDO

TDI

Debug Interface

MBIST Scan Chain

Debug Scan Chain

CPU

+

CPU Development Interface

CPU

+

CPU Development Interface

CPU n

CPU 1

CPU sub-module

MUX

ID

FSM

TAP Controller

MUX

MUX logic

WISHB. sub-module

Optional sub-modules

FSM

MUX

Reg.

CRC

Logic

MUX

FSM

Logic