Wishbone Outport
From B3 Specification

#### Author: Andrew Mulcock
amulcock@opencores.org

Rev. 0.1
2 February 2008

Not so much a specification, but cuttings from the

WISHBONE System-on-Chip (SoC)
Interconnection Architecture
for Portable IP Cores
Revision: B.3, Released: September 7, 2002

All references et all acknowledged.

As at Feb 2008, this directory contains 5 VHDL files,

- WBMEM16X16.vhd
- WBMEM32X16.vhd
- WBOPRT08.vhd
- WBOPRT16.vhd
- WBOPRT32.vhd

WBMEM are two memories for the wishbone bus. 16X16 is 16 registers of 16 bits data, whilst 32X16 is 16 registers of 32 bit data. Single cycle read as per the Wishbone B3 specification examples, Appendix A7.

WBOPRT are three out port registers. 08, is 8 bits data, 16 is 16 bit data, and 32 is 32 bit data. As per Wishbone B3 specification Appendix A6.

Below are the pertinent extracts from the B3 specification.