PCI32tLite

PCI Target IP Core

Developer's Manual

User's Manual

Copyright (C) 2005­2022 Peio Azkarate
OpenCores	PCI32tLite IP Core

1 Introduction

The PCI32tLite IP core provides the funtionality of a PCI target. The core has been designed to permit interface between a PCI Master and simple WHISBONE Slaves, and fitting into smallest FPGA (about 200 LC's in ALTERA CYCLONE II FPGA).

Thank you for your interest in the "pci32tlite_oc" IP Core. I'll be grateful with your feedbacks, good or bad. They will help to improve the IP Core.

Document History

Revisión		Descripción	Autor	Fecha

R00B00	First Beta release ­PRELIMINARY­.		Peio Azkarate	2005­05­12

R00	First release		Peio Azkarate	2006­07­17

R01	·	Added information for the R02 of the IPCore	Peio Azkarate	2007­09­19
	·	Added "pcmip_dbg" example project.
R01B00	·	Added information for the R02 of the IPCore	Peio Azkarate	2007­09­19
	·	Added "pcmip_dbg" example project.
R02	·	Added information for the R03 of the IPCore	Peio Azkarate	2008­06­16
	·	Changed BURST operation
	·	Added PCI32TLITE_HOWTO projects reference
	·	Removed "pcmipdbg_uart" project reference
	·	Change on PCI to WB data bus translation for BIG/16 (due to a
		bug fix).
R03	·	Remove PCI32TLITE_HOWTO information.	Peio Azkarate	2022-01­19

OpenCores	PCI32tLite IP Core

2 Features

FEATURES

WHISBONE compatible.

32 bits TARGET PCI Bus interface

MASTER WHISBONE; with configurable data bus size, 32/16/8 bits and configurable endianness, "BIG"/"LITTLE".

PCI Bus is Little endian.

Configuration Space Registers are Little endian.

PCI Configuration Space Register transactions could be BYTE/WORD/DWORD.

Supported BURST transactions.

BAR0 register, occupies 32Mbytes on PCI memory map for "1BARMEM" configuration.

BAR0 register, occupies 512Bytes on PCI I/O map for "1BARIO" configuration.

Supported commands are:

  - Memory Read

  - Memory Write

  - Configuration Read

  - Configuration Write

Target initiated Termination (RETRY)

FPGA Proven.
OpenCores	PCI32tLite IP Core

3 Description

INTERCONECTION

IP Interface Signals

Configuration

PCI32TLITE - Configuration Generics

Name		Type	Polarity	Description
vendorID	generic	std_logic_v	­­	PCI Vendor ID
deviceID	generic	std_logic_v		PCI Device ID
revisionID	generic	std_logic_v	­­	PCI Revision ID
subsystemID	generic	std_logic_v	­­	PCI Subsystem ID
subsystemvID	generic	std_logic_v	­­	PCI Subsystem Vendor ID
BARS	generic	string	­­	"1BARMEM"/"1BARIO"
WBSIZE	generic	integer	­­	Bus Whisbone SIZE: 32/16/8
WBENDIAN	generic	string	­­	Bus Whisbone Endianess: "BIG"/"LITTLE"

Control

PCI32TLITE - Control signals

Name	Type	Polarity	Description
rst	input	High	Reset. Active High, ¡ be careful ! the PCI "rst" signal
			is active Low.
PCI Target
	PCI32TLITE - PCI target signals
Name	Type	Polarity	Description
clk33	input	­	PCI Clock 33Mhz
ad[31..0]	bidir	­	PCI Address/Data
cbe[3..0]	input	Low	PCI Command/Byte enable
par	bidir	Low	PCI parity. numero de 1's en ad[31..0], cbe[3..0] y
			par debe ser un numero "par".

OpenCores			PCI32tLite IP Core

frame	input	Low	PCI frame. Indicate a bus transaction begin. When
			deasserted, the transaction is in the final data phase
			or has completed.
irdy	input	Low	Initiator ready. Indicates the bus master ability to
			complete the current data phase of the transaction.
trdy	output	Low	Target ready. Indicates the target ablility to complete
			the current data phase of the transaction.
devsel	output	Low	Device select. Target indicates to master that it has
			decoded its address.
stop	output	Low	The target is requesting the master to stop the
			current transaction.
idsel	input	Low	Initialization Device Select. Chip select for
			configuration transactions.
perr	output	Low	PCI Parity error
serr	output	Low	PCI System error
intb	output	Low	PCI Interrupt B
Whisbone Master
	PCI32TLITE - Whisbone master signals
Name	Type	Polarity	Description
wb_adr_o[24..0]	output	­	Whisbone address
wb_dat_i[(WBSIZE­1)..0]	input	­	Whisbone data in
wb_dat_o[(WBSIZE­1)..0]	output	­	Whisbone data out
wb_sel_o[((WBSIZE/8)­1)..0]	output	High	Whisbone data byte selection
wb_we_o	output	High	Whisbone write enable
wb_stb_o	output	High	Whisbone data strobe
wb_cyc_o	output	High	Whisbone cycle
wb_ack_i	input	High	Whisbone acknoledge
wb_rty_i	input	High	Whisbone retry
wb_err_i	input	High	Whisbone error
wb_int_i	input	High	Whisbone interrupt

Note: The reset signal "rst" is not a PCI signal. "rts" is active high while the PCI RST# is active low.

COMPONENTS

Fichero	Descripción
pci32tlite.vhd	TOP structural
pcidec.vhd	Decoder
pciwbsequ.vhd	PCI to WB sequencer
pcidmux.vhd	Data mux
pciregs.vhd	Configuration Space Registers
pcipargen.vhd	Parity generation
onalib.vhd	Small common functions.

PCIDEC

PCI decoder.
OpenCores	PCI32tLite IP Core

Registering address and command signals. Decode access to Configuration Space Register and to the PCI memory map.

PCIWBSEQU

PCI to WHISBONE sequencer. Translates transactions fron PCI to WHISBONE. Generate control signals for others blocks.

PCIDMUX

Multiplex WHISBONE and Configuration Space Registers data bus.

Registering WHISBONE data bus.

Transalates the 32 bits PCI data bus to 8/16/32 bits WHISBONE data bus.

PCI Little endian	WB byte swapping when Big endian.

PCIREGS

PCI registers. Configuration Space registers.

PCIPARGEN

Target parity generation on read transactions.
OpenCores	PCI32tLite IP Core

4 Implementation

PCI-WHISBONE Address map translation

PCI (AD24..AD2) address are translated to WHISBONE wb_adr(24..2). The WHISBONE address wb_adr(1) and wb_adr(0) are a logical combination from PCI CBE signals.

PCI-WHISBONE Big Endian-16 Bits

The PCI data bus size is 32 bits and the WHISBONE data bus is configurated as 16 bits.

The PCI bus is “Little endian” and WHISBONE is configured as “Big endian”.

Configuration Space Registers are “Little endian” and BYTE/WORD/DWORD accesses are possible.

Access from PCI to WHISBONE memory map (BAR0 32MBytes) should be done in BYTE/WORD.

The PCI to WHISBONE translation is "Address invariant translation". Address invaration mapping preserves the byte ordering of a data structure in a little ­endian memory map an a big­ endian memory map.

	PCI				WHISBONE				Byte lane
CBE(3)	CBE(2)	CBE(1)	CBE(0)	A1	A0	SEL(1)	SEL(0)	PCI	WB
0	0	0	0	0	0	1	1	D(15..0)	D(15..0)
1	1	0	0	0	0	1	1	D(15..0)	D(15..0)
0	0	1	1	1	0	1	1	D(31..16) D(15..0)
1	1	1	0	0	0	1	0	D(7..0)	D(15..8)
1	1	0	1	0	1	0	1	D(15..8)	D(7..0)
1	0	1	1	1	0	1	0	D(23..16) D(15..8)
0	1	1	1	1	1	0	1	D(31..24) D(7..0)

PCI-WHISBONE LITTLE ENDIAN-32 Bits Byte lane

	PCI				WHISBONE					Byte lane
CBE(3)	CBE(2)	CBE(1)	CBE(0)	A1	A0		SEL(3..0)				PCI	WB
0	0	0	0	X	X	1	1		1	1	D(31..0)	D(31..0)
				D(23..16)	D(7..0)
1	1	0	0	X	X	0	0		1	1	D(15..8)	D(15..8)
				D(7..0)	D(7..0)
0	0	1	1	X	X	1	1		0	0	D(31..24)	D(15..8)
				D(23..16)	D(7..0)
1	1	1	0	X	X	0	0		0	1	D(7..0)	D(7..0)
1	1	0	1	X	X	0	0		1	0	D(15..8)	D(15..8)

OpenCores	PCI32tLite IP Core

1	0	1	1	X	X	0	1	0	0	D(23..16)	D(7..0)
0	1	1	1	X	X	1	0	0	0	D(31..24)	D(15..8)

PCI-WHISBONE LITTLE ENDIAN-8 Bits Byte lane

	PCI				WHISBONE			Byte lane
CBE(3)	CBE(2)	CBE(1)	CBE(0)	A1	A0	SEL(0)	PCI	WB
0	0	0	0	0	0	1	AD(7..0)	D(7..0)
1	1	0	0	0	0	1	AD(7..0)	D(7..0)
0	0	1	1	1	0	1	AD(23..16) D(7..0)
1	1	1	0	0	0	1	AD(7..0)	D(7..0)
1	1	0	1	0	1	1	AD(15..8)	D(7..0)
1	0	1	1	1	0	1	AD(23..16) D(7..0)
0	1	1	1	1	1	1	AD(31..24) D(7..0)

Whisbone Configuration

The Whisbone data bus size and endianess can be configurated through WBSIZE and WBENDIAN VHDL generics. Allowed combination values for these generics are:
WBSIZE=32 WBENDIAN="LITTLE"

WBSIZE=16 WBENDIAN="BIG"

WBSIZE=8 WBENDIAN="LITTLE"

Whisbone RETRY

When a PCI transaction is terminated (on the WB bus side) with "wb_rty" instead a normal "wb_ack" termination. On PCI bus side, the STOP# signal is activated and produce a Target disconect termination.

BARS Configuration

BARS generic is available in order to configure BAR0 decoding response. "1BARMEM" option configures BAR0 for use 32MBytes on PCI Memory map. "1BARIO" option configures BAR0 for use 512Bytes on PCI IO map.

PCI BURST

PCI BURST transactions are terminated by target with "termination with..." so burst transactions are broken into individual transactions and they aren't traslated to whisbone bus as burts. This is a transparent feature for the whisbone slaves, and it's responsability to the PCI Compatible Master Controller/Bridge convert burst into individual cicles.
OpenCores	PCI32tLite IP Core

CONFIGURATION SPACE REGISTERS

The Configuration Registers from 0x00 to 0x3C conform with the PCI Device Configuration Header Format.

pci32tLite - PCI Configuration Space Registers layout

Address	Byte
	3	2	1	0

0x00	Device ID (generic)		Vendor ID (generic)
0x04	Status Register		Command Register
0x08	Class Code (0x068000)			Revision ID
				(generic)

0x0C	BIST	Header Type	Latency Timer	Cache Line
				Size

0x10	BAR0
0x14	This register is always 0.

0x18	This register is always 0.

0x1C	This register is always 0.

0x20	This register is always 0

0x24	This register is always 0

0x28	Card Bus CIS Pointer

0x2C	Subsystem ID (generic)		Subsystem Vendor ID (generic)
0x30	Expansion ROM Base Address Register

0x34	Reserved

0x38	Reserved

0x3C	Maximum	Minimum Grant	(0x01 INTA)	Interrupt Line
	Latency

Register	Addr	Offset		Byte Enable	Size
VENDORID	000000	00	0/1 (r)		WORD
DEVICEID	000000	02	2/3 (r)		WORD
CMD	000001	04	0/1 (r/w)		WORD
ST	000001	06	2/3 (r/w*)		WORD
REVISIONID	000010	08	0	(r)	BYTE
CLASSCODE	000010	09	1/2/3 (r)		3 BYTES
HEADERTYPE	000011	0E	2	(r)	BYTE
BAR0	000100	10	0/1/2/3 (r/w)		DWORD
INTLINE	001111	3C	0	(r/w)	BYTE
INTPIN	001111	3D	1	(r/w)	BYTE
(W*) reseteable

VENDORID ­ Vendor ID Register (r)

Identifies manufacturer of device. To configure by "generic".

DEVICEID ­ Device ID Register (r)
OpenCores	PCI32tLite IP Core

Identifies the device. To configure by "generic".

CMD ­ Command Register (r/w)

15	14	13	12	11	10	9	8
x	x	x	x	x	x	x	SERRENb

7	6	5	4	3	2	1	0
x	PERRENb	x	x	x	x	MEMSPENb	x

|

Reset value = 0x0000

SERRENb : System ERRor ENable (1 = Enable, 0 = Disable)

PERRENb : Parity ERRor ENable (1 = Enable, 0 = Disable)

MEMSPENb : MEMmory SPace ENable (1 = Enable, 0 = Disable)

ST ­ STatus register (r/w*)

15	14	13	12	11		10	9	8
PERRDTb	SERRSIb	x	x		TABORTSIb	DEVSELTIMb[1..0]			x

7	6	5	4		3	2	1		0
x	x	x	x		x	x	x		x

Reset value = 0x0200

PERRDTb : Parity ERRor DeTected (1 = Error Detected)

PERRSIb : System ERRor Signaled (1 = Error Signaled)

TABORTSIb : Target ABORT Signaled (1 = Abort Signaled)

DEVSELTIMb : DEVSEL Timing (01 = Medium)

Reads to this register behave normally. Writes are different, that bits can be cleared, but not set. Write a 1 to clear one bit.

REVISIONID ­ Revision ID Register (r)

Identifies a device revision.

CLASSCODEID ­ CLASS CODE Register (r)

Identifies the generic function of the device.

HEADERTYPE ­ HEADER TYPE Register (r)

Identifies the layout of the second part of the predefined header.
OpenCores	PCI32tLite IP Core

BAR0 ­ Base Address 0 Register (r/w)

31	30	29		28		27	26	25	24
			BAR032MBb[6..0]						0

23

22

21

20

19

18

17

16

0x00

15

14

13

12

11

10

9

8

0x00

7

6

5

4

3

2

1

0

0x00

Reset value = 0x00

BAR032MBb : Base Address 32MBytes decode space (7 bits)

SUBSYSTEMID ­ Subsystem ID Register (r)

Identifies the add­in board or subsystem where th PCI device resides. To configure by "generic".

SUBSYSTEM VENDORID ­ Subsystem Vendor ID Register (r)

Identifies the vendor of the add­in board or subsystem where th PCI device resides. To configure by "generic".

INTLINE ­ Interrupt Line Register (r/w)

7	6	5	4	3	2	1	0

INTLINEr[7..0]

Reset value = 0x00

INTLINEr : Defines interrupt line routing

INTPIN ­ Interrupt Pin Register (r)

7

6

5

4

3

2

1

0

0x01

Reset value = 0x01

INTPINr : Tells which interrupt pin the device uses. 0x01=INTA
OpenCores	PCI32tLite IP Core

5 FPGA proven

The pci32tLite_oc IP core has been tested in hardware, several project have been implemented in FPGA.

OpenCores	PCI32tLite IP Core

6 LICENSE

This source files may be used and distributed without restriction provided that this copyright statement is not removed from the files and that any derivative work contains the original copyright notice and the associated disclaimer.

This source files are free software; you can redistribute it and/or modify it under the terms of the GNU Lesser General Public License as published by the Free Software Foundation; either version 2.1 of the License, or (at your option) any later version

This source is distributed in the hope that it will be useful, but WITHOUT ANY WARRANTY; without even the implied warranty of MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the GNU Lesser General Public License for more details.

You should have received a copy of the GNU Lesser General Public License along with this source; if not, download it from http://www.opencores.org/lgpl.shtml.

Copyright (C) 2005­2008 Peio Azkarate, peio.azkarate@gmail.com