Power sequencer

V 1.00 2010-oct-15
© 2010.. Gerhard Hoffmann opencores@hoffmann–hochfrequenz.de
Published under BSD license

Large electronic systems often use multiple supply voltages that must come up and go down in a specified order. Also, it must be made sure that the system is not powered up only partly for a prolonged time.

This power sequencer obeys these rules:

Power supplies may be switched on at different times. The PS that runs the sequencer logic must be the very first, obviously. For every other supply or simultaneously switched group there is a sequencer slice. All slices are identical and daisy-chained to the next one.

The Voltage that goes on first will go off latest.
The voltage that goes on last will be the first to be switched off.
A new stage will be enabled only if so far everything is OK.
If a supply does not come up in time, an ordered retreat is made.
If a supply dies, a retreat is made from the end of the chain.
A failure is signaled until the power up request is removed.
There is an early failure indication if any supply fails so data may be saved.

Do not forget to attach pull down resistors to the PS enables, in case the sequencer is implemented in an FPGA that may not come up itself.

Components

1. PowerSequencer.vhd : the slice itself. It is replicated as often as needed.
2. retrigg_timer.vhd: a retriggerable timer that is used by the Sequencer slice.
1. PowerSequencer_tb.vhd: test bed that shows how the slices are interconnected
2. PowerSupply.vhd: A simple test bed model of a power supply that can declare itself faulty on command.
3. clk_rst.vhd: clock and reset generator for the testbed.
4. Makefile: creates the distribution tape
5. *.do- files commands for the modelsim simuator to run the simulation.
6. Typically, all subcomponents have test beds of their own.
7. *.png files screen shots of the simulator wave output.

How to interconnect the slices and power supplies.

State diagram of the sequencer

Waveform generated by simulation.

Zoom into Power Up

Zoom into Power Down

The power supply in the middle of the chain declares itself faulty at t = 90 msec.

Retriggerable timer

Power Supply